## Slide 1: INVESTIGATE THE MISALIGNMENT BETWEEN POINT CLOUD AND PERSPECTIVE IMAGE
Final Project CS 513 Geospatial Vision/Visualization

## Slide 2: TEAM MEMBERS
Adarsh M V – A20424847
Harshitha Rangaswamy – A20400223
Prerna Kumari – A20428292
Rahul Hosmani – A20418527

## Slide 3: Requirements
Programming Language: Python
  Python libraries:
    Math
    CV2
    Numpy
    Pandas
    Skimage
  Mesh Lab

## Slide 4: Input Data
Camera Configuration
Camera Information
Latitude, Longitude, Altitude, Quaternion S, Quaternion X, Quaternion Y, Quaternion Z
Perspective Image
Images from camera. The Field of View (FOV) is 90 degrees (Assuming no distortion).
Front, Back, Left and Right
Point Cloud
Point Cloud Data
Latitude, Longitude, Altitude, Intensity

## Slide 5: Objectives
  Extract the given information form the input data files
  Process the data and perform Coordinate Transformations.
    Step 1: LLA to ECEF
    Step 2: ECEF to ENU
    Step 3: ENU to Camera Coordinates
    Step 4: Camera Coordinates to Image Coordinates
  Lastly, Calculate the Misalignment angle between the point cloud and the perspective images.
  Glossary:
    LLA – Latitude Longitude Altitude
    ECEF – Earth Centered, Earth Fixed
    ENU – East North Up

## Slide 6: World Geodetic System – Earth Model
  Polar Radius = 6356752.3142 m
  Equatorial Radius = 6378137 m
WGS 84 (aka WGS 1984, EPSG:4326), established by US Department of Defense in 1984 and last revised in 2004, now being used in Global Positioning System (GPS)

## Slide 7: World Geodetic System – Latitude and Longitude
  λ = longitude
  Φ = geodetic latitude
  Flattening of earth ~= 1/298

## Slide 8: World Geodetic System –Altitude
  h – Altitude
  Φ – Geodetic Latitude

## Slide 9: Earth-Centered, Earth-Fixed (ECEF)
A unified geodetic Cartesian coordinate system.
Intermediate step in converting velocities from WGS coordinate to the local tangent coordinate system.

## Slide 10: Local Tangent Plane (LTP)
A local Cartesian coordinate system with a given origin.
Also called North East Down (NED), North East Up (NEU), Up North East (UNE)
Intermediate step in converting velocities from WGS coordinate to the camera coordinate system.

## Slide 11: Camera Coordinate
A local Cartesian coordinate system, origin is camera center.
Intermediate step in converting velocities from WGS coordinate to the image coordinate system.

## Slide 12: Relation between all the Coordinate Transformations

## Slide 13: Point Cloud
  A point cloud is a data structure used to represent a collection of multi-dimensional points and is commonly used to represent three-dimensional data.
  Points represent the X, Y and Z geometric Coordinates along with the intensity of the point on the sampled surface
These data points are produced by 3D scanners which measure a large number of points on the external surface of the objects around them. It can also be thought as collection of points that represent a 3D shape or feature.

## Slide 14: Coordinate Transformations
LLA
ECEF
ENU
Camera Coordinates
Image Coordinates

## Slide 15: Mathematics: Coordinate Transformation LLA to ECEF
Calculate ellipsoid flattening f.
  𝑓=
Calculate eccentricity e.
      𝑒=
Calculate the distance N from the surface to z- axis along ellipsoid normal as a function of 𝛷 (geodetic latitude):
  𝑁(𝛷)=
The ECEF coordinates X, Y and Z can be calculated from:
  𝑋=(ℎ+𝑁(𝛷)) cos⁡(𝜆) cos⁡(𝛷)
  𝑌=(ℎ+𝑁(𝛷)) cos⁡(𝜆) sin⁡(𝛷)
  𝑍=(ℎ+(1−𝑒^2)𝑁(𝛷)) sin⁡(𝜆)

## Slide 16: Code Snippet : LLA to ECEF

## Slide 17: Mathematics: Coordinate Transformation ECEF to ENU
With given origin , the location of in East North Up Coordinate is:
Where R is the rotation matrix:
So the whole transformation is:
\

## Slide 18: Code Snippet : ECEF to ENU

## Slide 19: Mathematics: Coordinate Transformation ENU to Camera Coordinates
When our vehicle captures image, it also records camera unit quaternion , the orthogonal matrix is:
With , in camera coordinate is:

## Slide 20: Code Snippet : ENU to Camera Coordinates

## Slide 21: Mathematics: Coordinate Transformation Camera Coordinates to Image Coordinates
For example, given in camera coordinate, if z>0, z>|x| and z>|y|, then this point belongs to “front” face.
The pixel which this point projects on front cube image with resolution is:
Notice that image coordinate is X-Y-reversed with camera coordinate.

## Slide 22: Code Snippet : Camera Coordinates to Image Coordinates

## Slide 23: Point Cloud Visualization using MeshLab

## Slide 24: Perspective Images
Left Right Front and Back

## Slide 25: Point cloud of the perspective images after Transformation
Front Back Left Right

## Slide 26: Front Face of the Cube Point Cloud Mesh

## Slide 27: Back Face of the Cube Point Cloud Mesh

## Slide 28: Left Face of the Cube Point Cloud Mesh

## Slide 29: Right Face of the Cube Point Cloud Mesh

## Slide 30: Finding the misalignment between point cloud image and camera image
  We have used the Brute-Force matcher with SIFT descriptors and Ratio test in OpenCV
Brute-Force matcher is simple. It takes the descriptor of one feature in first set and is matched with all other features in second set using some distance calculation. And the closest one is returned.

## Slide 31: Results

## Slide 32: Future Work
  In this project, we use feature-based technique to investigate the misalignment between point cloud and perspective image. However, we found that the feature-based approach is not very intuitive and the result may changes with the extraction of different feature points. So in future work, we want to use direct-based technique to investigate the misalignment.

## Slide 33: References
  https://gssc.esa.int/navipedia/index.php/Transformations_between_ECEF_and_ENU_coordinates
  http://docs.opencv.org/trunk/dc/dc3/tutorial_py_matcher.html
  https://ww2.mathworks.cn/help/map/ref/ecef2enu.html
  https://www.programcreek.com/python/example/89342/cv2.drawMatchesKnn

## Slide 34: Thank you